Schematic and Board Layout Design Review Notes
TEAM BEING REVIEWED: TEAM #3
REVIEWING TEAM: TEAM #11
DATE: 11/7/18
Note: (D) = dealt with
- SCHEMATIC
  - CRITICAL
    - (D) Junction dot out of RESET microprofessor button
    - (D) RESET needs a 10k pull up
    - (D) What is UVCC?
    - (D) Add 100nF caps to VCC,VCC1,AVCC,AVCC1
    - (D) Double check UCAP
    - Microphone
    - (D) How much current does the servo need?
    - (D) Remove the regulator
    - (D) Use a wall wart for the servo
      - If using wall wart to power board, need diode from processor to servo.
    - Confirm HWB function and confirm current wiring is correct.
  - MAJOR
    - (D) Add value/name to IC1
    - (D) Use 1 – 3 mA for the LEDs
    - Rearrange wires and add busses for readability.
  - MINOR
    - (D) Change font to info layer
    - (D) Go for right angles
    - (D) Do I need a buffer for the microphone output? Is that output 0 – 3.3V? Check datasheet
    - Statement “all surface mount components are …”
    - Does it use arduino?
    - Test Points Everywhere
    - Label VCC as 5V
- LAYOUT
  - CRITICAL
    - Determine if VCC line width is correct.
    - Align N$13 signal wire to lead straight into pin on processor.
  - MAJOR
    - Move/re-arrange some wires for readability.
  - MINOR
    - None.
- Bill of Materials (BOM)
  - No issues