Schematic and Board Layout Design Review Notes
TEAM BEING REVIEWED: [TEAM #]
REVIEWING TEAM: [TEAM # and/or name of reviewer if not on a team]
DATE: [DATE]
Instructions:
1. Reviewed team explains the concept of operation of the project.
2. Reviewer reads through schematic, layout, and BOM attempting to answer basic questions such as: what is the power supply? What is this IC and what does it do? Does the layout make sense?
3. Reviewer reads through schematic, layout, and BOM looking for best practices, such as: Are there enough bypass caps? Are the traces the right thickness?
  1. Reviewers are encouraged to use the Schematic and Layout Checklists that are posted on the D2L site.
4. One person on the reviewed team interacts and answers reviewer’s questions. A different person on the reviewed team takes notes, organized in the format below.
  Note: (D) = dealt with
- SCHEMATIC
  - CRITICAL
    - (D) Junction dot out of RESET microprofessor button
    - (D) RESET needs a 10k pull up
    - (D) What is UVCC?
    - (D) Add 100nF caps to VCC,VCC1,AVCC,AVCC1
    - (D) Double check UCAP
    - Microphone
    - (D) How much current does the servo need?
    - Remove the regulator
    - Use a wall wart for the servo
  - MAJOR
    - Add value/name to IC1
    - Issue 2
    - Add
    - Use 1 – 3 mA for the LEDs
  - MINOR
    - Change font to info layer
    - Go for right angles
    - Do I need a buffer for the microphone output? Is that output 0 – 3.3V? Check datasheet
    - Statement “all surface mount components are …”
    - Does it use arduino?
    - Test Points Everywhere
    - Label VCC as 5V
- LAYOUT
  - CRITICAL
    - Issue 1
    - Issue 2
  - MAJOR
    - Issue 1
    - Issue 2
  - MINOR
    - Issue 1
    - Issue 2
- Bill of Materials (BOM)
  - Issue 1
  - Issue 2